## Slide 1: Fuzzy Logic
By Arseni Pertzovskiy

## Slide 2: What is Fuzzy Logic System?
Generally, we want a method of reasoning, that resembles type of human reasoning. This involve all intermediate possibilities between discrete values YES and NO.
This model must be built so that it is capable of dealing with vague information.
Fuzzy logic-based systems do precisely that; they excel where systems are particularly complex and have been used successfully in many applications ranging from voice and handwriting recognition to subway train speed control. Fuzzy Logic System was invented by Lotfi Zadeh.

## Slide 3: Crisp sets vs Fuzzy sets
Classical logic is based on the crisp set, where a group of distinct objects are considered as a collection.
Unlike crisp sets, a fuzzy set allows partial belonging to a set, that is defined by a degree of membership, denoted by µ, that can take any value from 0 (element does not belong at all in the set) to 1 (element belongs fully to the set).

## Slide 4: Logic operations Crisp sets vs Fuzzy sets

## Slide 5: The Basic Configuration of a Fuzzy System
CRISP INPUT
CRISP OUTPUT

## Slide 6: Simple Example

## Slide 7: INPUT: temperature of 18 degrees and humidity of 60%
A temperature of 18 degrees is:
0.48 Cold 0.29 Medium 0.00 Hot
And humidity of 60% is:
0.0 Wet 1.0 Normal 0.0 Dry

## Slide 8: Fuzzy Output
The output set is finally defuzzified using centre-of-gravity defuzzification and a crisp value of 36.814 is obtained to drive the fan.
Slow
Moderate

## Slide 9: A Graphical Representation of This Process
Temperature
Humidity
Cold
Medium
Wet
Normal
Slow
Medium

## Slide 10: Advantages
Generally, in this system, we can take imprecise, distorted, noisy input information
These logics are easy to construct and understand
Due to the flexibility of fuzzy logic, we can add and delete rules in the FLS system
Suitable to problems which do not have high accuracy.

## Slide 11: Links to sources
https://www.youtube.com/watch?v=TReelsVxWxg&t=3s
https://towardsdatascience.com/a-very-brief-introduction-to-fuzzy-logic-and-fuzzy-systems-d68d14b3a3b8
https://medium.com/simplex-internet-blog/introduction-to-fuzzy-logic-3664c610d98c
https://medium.com/verifyas/fuzzy-logic-explained-67c075c2b228
https://www.massey.ac.nz/~nhreyes/MASSEY/159741/Lectures/Lec2012-3-159741-FuzzyLogic-v.2.pdf